Overview

Manitoba Conservation has received a proposal pursuant to The Environment Act from the Pembina Valley Water Cooperative (PVWC) and invites public participation and comments in the review process by Monday, February 6th. Upon receipt of any comments and objections, the Director of the Environmental Assessment & Licensing Branch (Tracey Braun) may do any or all of the following things: (ie, these are discretionary options under the Environment Act)

- require more info from PVWC

- issue guidelines and instructions for the environmental assessment and require PVWC to carry out public consultation

- require PVWC to prepare and submit an assessment report

- conduct or cause to be conducted a review of the assessment report

- REQUEST THE MINISTER OF CONSERVATION (Stan Struthers) TO DIRECT THE CLEAN ENVIRONMENT COMMISSION TO CONDUCT A PUBLIC HEARING

The PVWC Ground Water Supply Pipeline Project.

The first phase (the current project under consideration at this point in time) is planning to move groundwater approximately 96 kilometers by pipeline from the Sandilands Provincial Forest to Morris, MB and then through the PVWS network, which supplies 45,000 customers in the south central area of Manitoba. The project objective is supposedly required to” alleviate water shortages during periods of drought or contamination due to accidental spills".

The Sandilands region is an ecological gem as it is the source of freshwater for five major watersheds in the province (Brokenhead River/Whitemouth River/Rat River/Seine River/Cooks Creek). It is also believed that the Sandstone and Carbonate Aquifers (two major bedrock aquifers in south central Manitoba), gets most of its recharge from the Sandilands upland area. The first phase wants to divert 50 litres/sec (or about 1200 acre-ft annually). PVWC's "ultimate annual water requirement" (not under consideration in this application, but mentioned in the proposal) is 300 liters/sec (or about 7300 acre-ft annually).

The proposal filed by PVWC barely meets the informational requirements of Regulation 163/88 (The Licensing Procedures Regulation) and does not constitute a full Environmental Impact Statement (EIS).

# Some deficiencies identified in the Proposal filed by PVWC

## The proposal admits that little is known about the groundwater resource in this area. It states that, “Given that the aquifer (the lower sand unit which is under consideration) system is essentially undeveloped and very little information is available on the response of the aquifer to pumping, the estimation of a safe or sustainable yield is considered unwarranted and imprudent at the time.

Details such as size or areal extent of the lower sand unit are not adequately identified. The annual recharge rate, crudely estimated to be 10,125 acre-ft, does not factor in discharges to surface water systems, such as rivers, streams and creeks in the area. Given that this area is situated at the headwaters of the Brokenhead, Whitemouth, Seine and Rat Rivers, the volume can be substantial in drier years. In this respect, a drought analysis has not been performed. Therefore, a sustainable annual yield has not been calculated. Interactions (hydraulic transmissivity) between the upper sand unit and the sandstone unit (two other identified aquifers above and below the lower sand unit) are dismissed. This leads the proponent to conclude that no impacts will occur to the surface environment from the continuous withdrawal and in particular the Pocock Lake Ecological Reserve, which is approximately 1.5 kilometers north of the well site.

The proposal fails to provide an accurate reason why the PVWC requires more water. Current water use figures (or water budget) for the PVWC supply region are not provided as well as predictions for future use. Sam Schellenburg (CEO, PVWC) admits that over 50% of water consumed in the distribution network is within the agricultural sector. Alternative water supply options, including water soft paths and demand side management are not provided in the proposal.

The public involvement program invoked by PVWC was deficient, as it only involved municipal officials.

This proposal, if licensed, sets a precedent, which would allow others to extract water from this significant aquatic ecosystem. The Agassiz Sandilands Uplands area is an extensive aquifer complex that extends from the Trans Canada Highway to the US border and from the Bedford Ridge to near Lake of the Woods. Any removal or diversion of water from this region into the Red River sub-basin may violate the Water Resources Protection Act, as certain portions of the aquifer may be situated in the Winnipeg River and/or Lake Winnipeg sub-basins.

# Conclusion

Given that larger public policy issues have not been addressed, a rational for expanding the water supply was not provided and the sustainability of the aquifer was not adequately addressed, the Director of Environmental Assessment & Licensing should be encouraged to request Minister Struthers to conduct a Clean Environment Commission hearings.

January 24, 2006                                                                                      Via Facsimile

Tracey Braun, Director

Environmental Assessment & Licensing Branch

Manitoba Conservation

Suite 160 – 123 Main Street

Winnipeg, Manitoba R3C 1A5

945-5229 (f)

Honourable Stan Struthers

Minister of Conservation

Legislative Building

450 Broadway Avenue

Winnipeg, Manitoba R3C 0V8

945-3586 (f)

RE: PEMBINA VALLEY WATER COOPERATIVE INC. – SUPPLEMENTAL GROUNDWATER SUPPLY SYSTEM (Public Registry File 5156.00)

Dear Ms Braun and Mr. Struthers:

We have briefly reviewed the proposal to divert 50 L/s of water from the Sandilands area to Morris and eventually into the Pembina Valley Water Cooperative (PVWC) water distribution network. The proposal appears to be deficient as it barely meets the informational requirements as set out by Manitoba Regulation 163/88. We are very concerned with PVWC’s intent and request you to direct the Clean Environment Commission to conduct a public hearing for this project. Briefly, some of our reasons are as follows:

- The Agissiz Sandilands Uplands is an ecological gem and is the source of five major watersheds in the province (Brokenhead River/Whitemouth River/Rat River/Seine River/Cooks Creek). Kennedy and Woodbury (2005) also suggest that the Sandstone and Carbonate Aquifers (two major and very important aquifers in south central Manitoba) obtains most of its recharge from the Sandilands Uplands area.

- The proposal admits, “Given that the aquifer system is essentially undeveloped and very little information is available on the response of the aquifer to pumping, the estimation of a safe or sustainable yield is considered unwarranted and imprudent at the time.”  These information gaps include:

- Areal extent of the lower sand unit (the proposed aquifer to be tapped into).

- Discharge rates to surface water systems are not factored into the estimated annual recharge rate.

- Dismissal of interactions between the upper sand unit aquifer and lower sand unit aquifer, which may have an impact on the surface environment. This is of particular concern as the Pocock Lake Ecological Reserve is approximately 1.5 kilometers north of the well site.

- A drought analysis has not been performed.

- The approximately 96 kilometers of pipeline will cross numerous rivers, streams and creeks and will invariably impact fish habitat areas.

- The proposal fails to provide an accurate reason why PVWC needs more water. Current water use figures (or water budget) for the PVWC supply region are not provided nor are predictions for future use. Alternative water supply options, including soft paths and demand side management are not provided in this proposal.

- The public involvement program invoked by PVWC was deficient, as it limited participation to municipal officials.

- Larger public policy issues have not been addressed. These include:

- Setting precedence for allowing other large users to extract water from this significant aquatic ecosystem.

- Removing and diverting water from one sub-basin to another as certain portions of the aquifer may be situated in the Winnipeg River and/or Lake Winnipeg sub-basins. This would be a direct violation of the Water Resources Conservation Act.

- Source protection measures as proposed through the Water Protection Act, have not been enabled, which could positively affect the availability of clean water in the PVWS distribution area.

- Manitoba Water Stewardship has placed heavy emphasis on watershed planning. The proposal does not take into account what plans are in place and what plans are to be developed.

- The requirement to set a minimum instream flow on the Red River at the US/Canada border.

As well as calling for a Clean Environment Commission hearing, we request the proponent to develop a full Environmental Impact Statement (EIS) and request participation in the development of guidelines for the preparation of the EIS.

Sincerely

G.R. Koroluk 775-7848

Friends of the Pocock Lake Ecological Reserve

609 Main Street

Winnipeg, Manitoba R3B 1E1

cc.

Honourable Steve Ashton, Minister of Water Stewardship

Dan McNaughton, Director, Prairie Office – Canadian Environmental Assessment Agency

Chief Tina Leveque, Brokenhead First Nation

Chief John Thunder, Buffalo Point First Nation

# Footnotes

Kennedy, P and Woodbury, A., Sustainability of the Bedrock Aquifer Systems in South-Central Manitoba: Implications for Large-Scale Modeling Canadian Water Resources Journal, Vol 30(4) 281-296 (2005).